## Slide 1: Order Picking Operations
Chapter 8 Warehouse management

## Slide 2: Operating Cost Distribution
Chart: 
| Shipping | Receiving | Storage | Picking
Warehouse Function | 0.15 | 0.15 | 0.2 | 0.5

## Slide 3: Order Picking Operations
63% of all operating costs
   picking
Most labor intensive function
   picking
Most material and handling equipment
   picking
Most Decision Support & engineering project
   picking
Most Warehouse Errors
   picking

## Slide 4: Picking Challenges
(JIT) Just in Time
Cycle Time Reduction
Quick Response
Micromarketing
Megabrand Strategies
More frequent smaller orders
More SKU’s

## Slide 5: Picking Strategies
Issue pack optimization
Pick-from-storage
Pick task simplification
Order batching
Slotting optimization
Pick sequencing

## Slide 6: Bar Code License Plates

## Slide 7: I. Issue Pack Optimization
Match the storage unit to the shipping unit

## Slide 8: II. Pick from Storage
Reserve Storage & Pallet Picking
Case Picking
RECEIVING
Broken Case Picking
Customization
SHIPPING
Direct Put away
Direct Put away
Crossdock
Replenishment
Picking

## Slide 9: III. Pick Task Simplification
Eliminate and combine order picking tasks when possible
Traveling | Extracting | Reaching & Bending
Documenting | Sorting | Picking
Searching |  | 

## Slide 10: Distribution of Order Pickers Time
Chart: Picking Time
| Travelling | Searching | Extracting | Other
Picking | 0.55 | 0.15 | 0.1 | 0.2

## Slide 11: Picking Work Elements
Work Element | Method Elimination | Technology/Function
Traveling | Bring pick loc to picker | Stock to picker system; ASRS/ Carousel
Documenting | Auto info flow | Computer aided picking/ light aided pick/RF Terminals/Headsets
Reaching | Present items at waist level | Carousel/ASRS
Searching | Illuminate pick locs, bring pick loc to picker | Stock to picker systems/Pick to light/ASRS
Extracting | Automated dispensing | Auto item pickers/robotics
Counting | Weigh counting/prepackage | Scales on pick vehicles
Restocking | Auto look-ahead | Min-max triggers
Excessive Socializing | Assign operators to dedicated zones | 
Idling/waiting for work | Dynamic zone sizing/perpetual to-do lists | 

## Slide 12: IV. Order Batching
Increasing the number of orders picked by an order picker during a pick tour.

## Slide 13: Zone Picking
Pro’s
Travel time is reduced
Operators familiarity with material
Congestion is minimized
Zone accountability
Minimizes socializing

## Slide 14: V. Slotting Optimization
For each Item Determine:
  Appropriate storage mode
  Appropriate allocation of space
  Appropriate storage location
Slotting impacts all of the KPI’s: productivity, shipping accuracy, inventory accuracy, dock-to-stock time, warehouse order cycle time, and storage density,

## Slide 15: Slotting Methodology
Conduct a warehouse operations audit
Populate the slotting database
Compute slotting statistics
Construct the warehouse profile
Assign items to item families
Assign item activity families to storage mode families
Map the warehouse locations within each storage mode
Based on pick density, assign items to mode activity zones
Specify reslotting rules

## Slide 16: VI. Pick Sequencing
Start